## Slide 1
School of E&EE
FACULTY OF ENGINEERING
Data Communications and Network Security
ELEC5471M
Section 3. The Network Layer and IP.

## Slide 2: Data Communications and Network Security
Learning Objectives To provide students with a knowledge and understanding of data communications and wireless sensor networks and how they are, and could be, used in a range of applications. (See module catalogue).
I will cover these objectives by:
  Introductory lecture and the ISO/OSI 7-layer protocol architecture.
  The Internet and the TCP/IP architecture.
  You will examine the transport layer and in particular TCP and UDP.
  Examining the way in which security can be provided across networks will be considered.
  We’ll consider the functions of the network layer and IP.
  We will develop methods of sharing a common transmission medium (MAC).

## Slide 3: Data Communications and Network Security
What must you contribute?
  Lectures will be the basic provision of material but YOUR private study is also required.
  Also you need to do the web examples suggested, you need to read from all the advised texts and consult the other suggested texts.
  You must spend time before each lecture preparing yourself for what the lecture will be about and after each lecture going over the content and checking your understanding.
The Assessment of the module:
  Will check you have all met the learning objectives.
  Will grade to what extent you have exceeded the objectives.
The exam questions I set will be on:
  The layered protocol architectures (ISO and TCP/IP).
  The transport layer and sessions across a network, TCP & UDP operation (including congestion control).
  Network layer issues (including addressing and routing).
  Link layer issues (e.g. MAC).
There will also be a project on the security aspects.

## Slide 4: Data Communications and Network Security ELEC5471M
To be given by:
  Prof A. H. Kemp
  Possibly with support from experts studying in the field.
Assessment will be by 1 exam of 3 hours duration.
Advised texts:
  Computer Networking by Kurose and Ross ISBN:0201976994
  Protocols and architectures for wireless sensor networks by Holger, K. and Willig, A. Hoboken, NJ : Wiley, 2007, c2005.
  Computer Networks, by Tanenbaum ISBN:0133499456
  Multimedia communications by Halsall ISBN:0201398184
Also for general reading:
  Data & Computer Communications, by Stallings ISBN:0135712742

## Slide 5: The Network Layer & Internet Protocol
Addressing
IPv6 (& IPv4 interoperability)
Routing (link-state, distance vector, Internet, Routers)

## Slide 6: The Network Layer & Internet Protocol
IP Addresses
  Addressing over the Internet is a crucial issue.
  IPv4 is prevalent and several addressing schemes exist.
  IPv6 has been defined and introduced and will soon become dominant across the Internet. It has a different addressing solution.
Internet Protocol

## Slide 7
Context:

## Slide 8: The Network Layer & Internet Protocol
Addressing
  Each host, gateway, router (interface) has a unique Internet-wide IP address assigned to it.
  The address can be broken down into a net-id and a host-id.
  IPv4 defines a 32-bit address space and 4 schemes have been used to better utilize this. A fifth scheme uses a wider address space.
Internet Protocol

## Slide 9: Net-work layer context

## Slide 10
IPv4 datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
Internet
checksum
time to
live
32 bit source IP address
IP protocol version
number
header length
(bytes)
max number
remaining hops
(decremented at
each router)
for
fragmentation/
reassembly
total datagram
length (bytes)
upper layer protocol
to deliver payload to
head.
len
type of
service
“type” of data
flgs
fragment
offset
upper
layer
32 bit destination IP address
Options (if any)
E.g. timestamp,
record route
taken, specify
list of routers
to visit.

## Slide 11
IPv4 32-bit addresses
  Class-based addresses. (5 address classes)
  Subnetting. (To allow single address per site)
  Classless addresses. (Removed fixed class boundaries)
  Network address translation. (NAT; assigns single IP address per access network).
IPv6 128-bit addresses
  Massive increase in addresses.
Internet Protocol, addressing schemes
Notes: 2^32 = 4292967296 = 4.3 x 10^9 =4,000 million
2^128 = 3.40282366920… x 10^38 = 300 million million million million
million
million.

## Slide 12
IPv4 addresses are referred to by dotted decimal notation.
  The 32-bit address is broken in 4 bytes.
  Each byte is converted to decimal.
  The address is referred to as four decimal numbers with full-stops (periods) between them.
  10000000 00000011 00000010 00000011 = 128.3.2.3
  This is class B, netid 128.3 and hostid 2.3
Internet Protocol, addressing schemes

## Slide 13
Class-based addresses
  32-bit address divided into five classes A, B, C, D, E:
Internet Protocol, addressing schemes

## Slide 14
Dotted decimal notation example:
previously
Internet Protocol, addressing schemes

## Slide 15
previously
Internet Protocol, addressing schemes

## Slide 16: Class-based addresses
Classes A, B & C are for unicast, D for multicast and E is reserved.
Class A has a 7-bit Net-ID field and 24-bit Host-ID field.
Class B 14-bit Net-ID field and 16-bit Host-ID field.
Class C 21-bit Net-ID field and 8-bit Host-ID field.
Host-IDs of all 0s or 1s are special:
  0s refers to network (in the Net-ID)
  1s means broadcast the packet over the destination network (in the NetID part).
Net-IDs of all 0s or 1s are special:
  0s means the same network as the source network (NetID).
  Address of all 1s means broadcast the packet over the source network.
Internet Protocol, addressing schemes

## Slide 17: Class-based addresses
Class D addresses are reserved for multicasting.
Assigned by ICANN
Mainly used for conferences etc.
Permanent multicast group addresses:
  224.0.1 : All hosts on broadcast network.
  224.0.2 : All routers on the same site network.
Internet Protocol, addressing schemes

## Slide 18
Subnetting.
  This is a method to reduce the required number of netids i.e. where many routers are used rather than MAC bridges.
  NetID now refers to a complete site (rather than a single subnet).
  Netid is Internet part.
  HostID consists of 2 subfields: subnetid and local hostid
  Routers on local site are subnet routers.
Internet Protocol, addressing schemes

## Slide 19
Internet Protocol, addressing schemes

## Slide 20
Classless addresses
  The definition of network part of the IP address can now be any number of bits.
  Address expressed in dotted decimal as w.x.y.z / n .
  Where n now indicates the number of bits in the network part of the address.
  E.g. if a network requires say 1000 host addresses it can have address w.x.y.z/22 i.e. the first 22 bits represent the netid and the last 10 bits the hostid.
  Uses Classless Inter-domain routing (CIDR)
Internet Protocol, addressing schemes

## Slide 21
Network address translation (NAT)
  This is basically a temporary fix as IP(v4) addresses are running out.
An intermediary (a NAT router or Access gateway) uses transport layer information to save on Network layer addresses!
A reserved number of IP addresses are kept as ‘private addresses’ i.e. addresses not to be used on the Internet.
TCP uses port addresses to indicate processes and in effect these are used to address the ‘private addresses’.
Internet Protocol, addressing schemes

## Slide 22
Network address translation:
a) blocks of private addresses,
b) NAT operation,
c) IP/TCP header fields.

## Slide 23
IPv6
  The long term solution to the chronic shortage of Internet addresses is the introduction of IPv6.
  Uses 128-bit address field.
  More IPv6 addresses than grains of sand on the planet!
Internet Protocol, addressing schemes

## Slide 24
The main features offered by IPv6 are:
  Increased address space (2128 addresses!)
  Hierarchical addresses
  Simplified header
  Improved security
  Autoconfiguration facility
  QoS guarantees
  Support of mobile computing
IPv6

## Slide 25
Compared to IPv4 a number of fields have been dropped or made optional.
Main/basic header is 40 bytes.
  Version: 6
  Traffic class is similar to ToS of IPv4. 4-bit priority
IPv6

## Slide 27
IPv6 not only offers more addresses it also provides better QoS support, more efficient service and better flexibility.
IPv6 position and order of extension headers:
Internet Protocol, addressing schemes
EH (1)

## Slide 28
IPv6 needs to exist with IPv4:
IPv6 addresses: (a) prefix formats and their use; (b) IPv4 address types
Internet Protocol, addressing schemes

## Slide 29
IPv6 addresses: (c) provider-based unicast address format; (d) multicast address format
Internet Protocol, addressing schemes

## Slide 30: Internet Protocol, IPv6 addressing
The way IPv6 addresses are written down:
IPv6 addresses are written as 8 groups, each of 16 bits.
Each group is represented as 4 hexadecimal characters.
Colons (:) separate the groups.
All zero groups (:0000:) are dropped and leading zeros are dropped.
E.g. 1111111011011100101110101001100001110110..
= FEDC:BA98:7654:3210:0000:0123:0000
Written as:
FEDC:BA98:7654:3210::123:

## Slide 31
Widespread deployment of IPv4 makes switch-off impractical.
3 different cases must be catered for:
  IPv4 and IPv6 hosts communicating with a single server.
  IPv6 source and destination communicating across IPv4 sections of network.
  IPv6 host communicating with an IPv4 host.
IPv4 and IPv6 Interoperability

## Slide 32
IPv6/IPv4 interoperability using dual (IPv6/IPv4) protocols
1. IPv4 and IPv6 hosts communicating with a single server

## Slide 33
IPv6/IPv4 interoperability using dual stacks and tunneling: (a) schematic
2. IPv6 source and destination communicating across IPv4 sections of network

## Slide 34
IPv6/IPv4 interoperability using dual stacks and tunneling: (b) protocols

## Slide 35
IPv6/IPv4 interoperability using translators: (a) network level
  3. IPv6 host communicating with an IPv4 host.

## Slide 36
IPv6/IPv4 interoperability using translators: (b) application level

## Slide 37: IP Summary items:
IPv4 and addressing
  Addressing: dotted decimal notation
  Classless, subnetting, NAT
IPv6
  Addressing, functions, operation
  8 Groups of 4 Hex digits.
  Interoperation with IPv4

## Slide 38: Key Network layer function: Routing
Routing (link-state, distance vector, Internet, Routers)
QoS Routing
Routing in Wireless Networks

## Slide 39: Network Layer
Introduction
What’s inside a router
IP: Internet Protocol
Routing algorithms
  Link state
  Distance-Vector

## Slide 40: What is “Routing”?
In computer networking, the term Routing refers to selecting paths in a computer network along which to send data.
Routing occurs at the Network layer (layer 3) of the OSI seven-layer protocol stack.
A Router is a computer networking device that forwards data packets across a network toward their destinations, through a process known as routing
Routing is the most important function of the network layer
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical

## Slide 41: Network Layer
Introduction
What’s inside a router
Routing algorithms
  Link state
  Distance-Vector

## Slide 42: Router Architecture Overview
Four components :
Input Ports, Switching Fabric, Output Ports and Routing Processor

## Slide 43: Where does Queuing Occur?
Input Port Queuing
  Fabric slower than input ports combined -> queuing may occur at input queues
  Queuing delay and loss due to input buffer overflow!

## Slide 44: Where does Queuing Occur?
  buffering when arrival rate (via switch) exceeds output line speed
  queuing can cause delay and loss due to output port buffer overflow!
Output port queuing

## Slide 45: Network Layer
Introduction
What’s inside a router
Routing algorithms
  Link state routing algorithm
  Distance-Vector algorithm

## Slide 46: Graph Abstraction
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Graph: G = (N,E)
N = set of routers = { u, v, w, x, y, z }
E = set of links ={ (u,v), (u,x), (u,w), (v,x), (v,w), (x,w), (x,y), (w,y), (w,z), (y,z) }
or edges, E.

## Slide 47
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
c(x,x’) = cost of link (x,x’)
- e.g., c(w,z) = 5
cost could always be 1, or
inversely related to bandwidth,
or inversely related to
congestion
Cost of path (x1, x2, x3,…, xp) = c(x1,x2) + c(x2,x3) + … + c(xp-1,xp)
Question: What’s the least-cost path between u and z ?
Routing algorithm: algorithm that finds least-cost path
Graph abstraction: costs

## Slide 48: Routing Algorithm classification
Global or decentralized information?
Global:
all routers have complete topology, link cost info
“link state” algorithms
Decentralized:
router knows physically-connected neighbours, link costs to neighbours
iterative process of computation, exchange of info with neighbours
“distance vector” algorithms
Static or dynamic?
Static:
routes change slowly over time
Dynamic:
routes change more quickly
  periodic update
  in response to link cost changes

## Slide 49: Network Layer
Introduction
What’s inside a router
Routing algorithms
  Link state
  Distance-Vector

## Slide 50: A Link-State Routing Algorithm
Dijkstra’s algorithm
net topology, link costs known to all nodes
  accomplished via “link state broadcast”
  all nodes have same info
computes least cost paths from one node (‘source’) to all other nodes
  gives forwarding table for that node
iterative: after k iterations, know least cost path to k destinations
Notation:
c(x,y): link cost from node x to y; = ∞ if not direct neighbours
D(v): current value of cost of path from source to dest. v
p(v): predecessor node along path from source to v
N': set of nodes whose least cost path definitively known

## Slide 51: Dijsktra’s Algorithm
1 Initialization:
2 N' = {u}
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N' :
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 shortest path cost to w plus cost from w to v */
15 until all nodes in N'

## Slide 52: Dijkstra’s algorithm: example
Step
0
1
2
3
4
5
N'
u
ux
uxy
uxyv
uxyvw
uxyvwz
D(v),p(v)
2,u
2,u
2,u
D(w),p(w)
5,u
4,x
3,y
3,y
D(x),p(x)
1,u
D(y),p(y)
∞
2,x
D(z),p(z)
∞
∞
4,y
4,y
4,y
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 53: Dijkstra’s algorithm: example (2)
u
y
x
w
v
z
Resulting shortest-path tree from u:
v
x
y
w
z
(u,v)
(u,x)
(u,x)
(u,x)
(u,x)
destination
link
Resulting forwarding table in u:
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5

## Slide 54: Dijkstra’s algorithm, discussion
Algorithm complexity: n nodes
each iteration: need to check all nodes, w, not in N
n(n+1)/2 Complexity:O(n2)

## Slide 55: Network Layer
Introduction
What’s inside a router
Routing algorithms
  Link state
  Distance-Vector

## Slide 56: Distance Vector (DV) Algorithm
A decentralized routing algorithm
Compared with LS, DV algorithm is iterative, asynchronous and distributed
No global information, each node only receives some information from one or more of its directly attached neighbours

## Slide 57: Distance Vector Algorithm
Bellman-Ford Equation (dynamic programming)
Define
dx(y) := cost of least-cost path from x to y
Then
dx(y) = min {c(x,v) + dv(y) }
where min is taken over all neighbours v of x
v

## Slide 58: Bellman-Ford example
u
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
Clearly, dv(z) = 5, dx(z) = 3, dw(z) = 3
du(z) = min { c(u,v) + dv(z),
c(u,x) + dx(z),
c(u,w) + dw(z) }
= min {2 + 5,
1 + 3,
5 + 3} = 4
Node that achieves minimum is next
hop in shortest path ➜ forwarding table
B-F equation says:

## Slide 59: Distance Vector Algorithm
Dx(y) = estimate of least cost from x to y
Distance vector: Dx = [Dx(y): y є N ]
Node x knows cost to each neighbour v: c(x,v)
Node x maintains Dx = [Dx(y): y є N ]
Node x also maintains its neighbours’ distance vectors
  For each neighbour v, x maintains Dv = [Dv(y): y є N ]

## Slide 60: Distance vector algorithm (4)
Basic idea:
Each node periodically sends its own distance vector estimate to neighbours
When a node x receives new DV estimate from neighbor, it updates its own DV using B-F equation:
Dx(y) ← minv{c(x,v) + Dv(y)} for each node y ∊ N
Under minor, natural conditions, the estimate Dx(y) converge to the actual least cost dx(y)

## Slide 61: Distance Vector Algorithm (5)
Iterative, asynchronous: each local iteration caused by:
local link cost change
DV update message from neighbour
Distributed:
each node notifies neighbours only when its DV changes
  neighbours then notify their neighbours if necessary
wait for (change in local link cost msg from neighbour)
recompute estimates
if DV to any dest has changed, notify neighbours
Each node:

## Slide 62
x y z
x
y
z
0 2 7
∞
∞
∞
∞
∞
∞
from
cost to
from
from
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
∞
∞
∞
∞
∞
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 3
from
cost to
x y z
x
y
z
0 2 7
from
cost to
x y z
x
y
z
∞
∞
∞
7
1
0
cost to
∞
2 0 1
∞ ∞ ∞
2 0 1
7 1 0
2 0 1
7 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
2 0 1
3 1 0
time
x
z
1
2
7
y
node x table
node y table
node z table
Dx(y) = min{c(x,y) + Dy(y), c(x,z) + Dz(y)} = min{2+0 , 7+1} = 2
Dx(z) = min{c(x,y) + Dy(z), c(x,z) + Dz(z)}
= min{2+1 , 7+0} = 3

## Slide 63: Distance Vector: link cost changes
Link cost changes:
node detects local link cost change
updates routing info, recalculates distance vector
if DV changes, notify neighbours
x
z
1
4
50
y
1
At time t0, y detects the link-cost change, updates its DV,
and informs its neighbours.
At time t1, z receives the update from y and updates its table.
It computes a new least cost to x and sends its neighbours its DV.
At time t2, y receives z’s update and updates its distance table.
y’s least costs do not change and hence y does not send any
message to z.

## Slide 64: Distance Vector: link cost changes
Link cost changes:
good news travels fast
bad news travels slow - “count to infinity” problem!
44 iterations before algorithm stabilizes: see text
Please read section 4.5.2 of Kurose & Ross (Ed. 4)
x
z
1
4
50
y
60

## Slide 65: Comparison of LS and DV algorithms
Message complexity
LS: with n nodes, E links, O(nE) msgs sent
DV: exchange between neighbours only
  convergence time varies
Speed of Convergence
LS: O(n2) algorithm requires O(nE) msgs
DV: convergence time varies
  may be routing loops
  count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  node can advertise incorrect link cost
  each node computes only its own table
DV:
  DV node can advertise incorrect path cost
  each node’s table used by others
    error propagate thru network

## Slide 66: Summary
How a router works
LS routing algorithm
DV routing algorithm