## Slide 1: ELEC5620M Embedded Microprocessor System Design
Unit 1.2 Pointers and Functions
Dr David Cowell Module Leader d.m.j.cowell@leeds.ac.uk
Prof Steven Freear

## Slide 2: Reference Textbooks - C
Practical C Programming
The C Programming Language
Minerva > ELEC5620M > Module Information > Module Reading List

## Slide 3: GitHub ELEC5620M-Resources
Minerva > ELEC5620M > General Resources > Lab Resources on GitHub

## Slide 4: GitHub ELEC5620M-Unit1
Minerva > ELEC5620M > Unit 1 > Unit 1 GitHub Classrooms Resources

## Slide 5: DE1-SoC Hardware Loan
You need the DE1-SoC hardware to complete the tasks and future assessments!

## Slide 6: Hardware Loan

## Slide 7: Hardware Loan

## Slide 10: Memory Mapped Peripherals Outputs - LEDs

## Slide 11: Memory Mapped Peripherals Outputs - LEDs
Why 16?
Think in binary… think in hexadecimal!
Use Windows Calculator – Programmer mode!
5th LED from right (LED4) illuminated!

## Slide 12: Memory Mapped Peripherals Outputs - LEDs
Why 16?
Think in binary… think in hexadecimal!
Use Windows Calculator – Programmer mode!
5th LED from right (LED4) illuminated!

## Slide 13: 1-1-HelloWatchdog main.c
int main(void) {
// Declare pointers to I/O registers
// (volatile keyword means memory not cached)
// WDT Current Value Register (l4wd0: wdt_ccvr)
volatile unsigned int *wdt_ccvr = (unsigned int *)0xFFD02008;
// WDT Counter Reload Register (l4wd0: wdt_crr)
volatile unsigned int *wdt_crr = (unsigned int *)0xFFD0200C;
// Red LEDs base address
volatile int *LEDR_ptr = (int *)0xFF200000;
// KEY buttons base address
volatile int *KEY_ptr = (int *)0xFF200050;
...

## Slide 14: 1-1-HelloWatchdog main.c
int main(void) {
// Declare pointers to I/O registers (volatile keyword means memory not cached)
volatile unsigned int *wdt_ccvr = (unsigned int *)0xFFD02008; // WDT Current Value Register (l4wd0: wdt_ccvr)
volatile unsigned int *wdt_crr = (unsigned int *)0xFFD0200C; // WDT Counter Reload Register (l4wd0: wdt_crr)
volatile unsigned int *LEDR_ptr = (unsigned int *)0xFF200000; // Red LEDs base address
volatile unsigned int *KEY_ptr = (unsigned int *)0xFF200050; // KEY buttons base address
// Primary Run Loop - Bare-Metal Applications use an infinite loop to keep executing (no OS).
while (1) {
// Read WDT counter value and display it on the red LEDs (scaled to fit).
*LEDR_ptr = *wdt_ccvr >> 16;
//Check if any of the buttons have been pressed.
//Each of the lower 4 bits represents one of the keys. A key is pressed if the corresponding bit is 1.
if (*KEY_ptr & 0xF) {
// If any key pressed
*wdt_crr = 0x76; // Reset the Watchdog Timer
}
}
}

## Slide 15: Watchdog Timer Reset
Challenge:
Use debugger and check the wdt_torr register to determine wdt_ccvr reset value.

## Slide 16: Watchdog Timer Reset
Challenge:
Use debugger and check the wdt_torr register to determine wdt_ccvr reset value.
26 bits

## Slide 19: 1-1-HelloWatchdog main.c
int main(void) {
// Declare pointers to I/O registers
// (volatile keyword means memory not cached)
// WDT Current Value Register (l4wd0: wdt_ccvr)
volatile unsigned int *wdt_ccvr = (unsigned int *)0xFFD02008;
// WDT Counter Reload Register (l4wd0: wdt_crr)
volatile unsigned int *wdt_crr = (unsigned int *)0xFFD0200C;
// Red LEDs base address
volatile int *LEDR_ptr = (int *)0xFF200000;
// KEY buttons base address
volatile int *KEY_ptr = (int *)0xFF200050;
...

## Slide 20: Bit shifting 1-1-HelloWatchdog - main.c
while (1) {
// Read WDT counter value, and display it on the red LEDs (scaled to fit).
*LEDR_ptr = *wdt_ccvr >> 16;
bit 31 30 29 28 27 26 25 24 23 22 21 20 19 18 17 16 15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0
*wdt_ccvr 0 0 0 0 0 0 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 1 0 0 0 0
16 lost bits
16 Zero Padding Bits
*wdt_ccvr>>16 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 1 1 1
Example of bit shifting – Lookup >> and << in reference texts.

## Slide 21: Memory Mapped Peripherals Inputs – Switches and Buttons

## Slide 22: 1-1-HelloWatchdog main.c
int main(void) {
// Declare pointers to I/O registers
// (volatile keyword means memory not cached)
// WDT Current Value Register (l4wd0: wdt_ccvr)
volatile unsigned int *wdt_ccvr = (unsigned int *)0xFFD02008;
// WDT Counter Reload Register (l4wd0: wdt_crr)
volatile unsigned int *wdt_crr = (unsigned int *)0xFFD0200C;
// Red LEDs base address
volatile int *LEDR_ptr = (int *)0xFF200000;
// KEY buttons base address
volatile int *KEY_ptr = (int *)0xFF200050;
...

## Slide 23: Memory Mapped Peripherals Inputs – Switches and Buttons

## Slide 24: Memory Mapped Peripherals Inputs – Switches and Buttons

## Slide 25: Bit masking 1-1-HelloWatchdog - main.c
/**
* Check if any of the buttons have been pressed.
* Each of the lower 4 bits represents one of the keys.
* A key is pressed if the corresponding bit is 1.
*/
if (*KEY_ptr & 0xF) {
// If any key pressed
*wdt_crr = 0x76; // Reset the Watchdog Timer
}
}
}
bit 31 30 29 28 27 26 25 24 23 22 21 20 19 18 17 16 15 14 15 13 12 11 10 9 8 7 6 5 4 3 2 1 0
*KEY_ptr X X X X X X X X X X X X X X X X X X X X X X X X X X X X X 0 0 0 1
0xF (0x000F) 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1
(*KEY_ptr & 0xF) 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1
A | B | A & B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 26: Bit masking 1-1-HelloWatchdog - main.c
/**
* Check if any of the buttons have been pressed.
* Each of the lower 4 bits represents one of the keys.
* A key is pressed if the corresponding bit is 1.
*/
if (*KEY_ptr & 0xF) {
// If any key pressed
*wdt_crr = 0x76; // Reset the Watchdog Timer
}
}
}
bit 31 30 29 28 27 26 25 24 23 22 21 20 19 18 17 16 15 14 15 13 12 11 10 9 8 7 6 5 4 3 2 1 0
*KEY_ptr 0 0 0 0 0 0 0 0 0 0 0 0 1 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1
0xF (0x000F) 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1
(*KEY_ptr & 0xF) 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1
Erroneous high bit defeated with bit masking!!!
A | B | A & B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 27: Unit 1.1 Task 3: HelloWatchdog – Reset on button release

## Slide 28: Unit 1.1 Task 3: HelloWatchdog – Reset on button release
while (1)
{
// Read WDT counter value, and display it on the red LEDs
*LEDR_ptr = *wdt_ccvr >> 16;
//Check if any of the buttons have been pressed.
if (*KEY_ptr & 0xF) // Key pressed?
{
while (*KEY_ptr & 0xF)
{
// Key still pressed - update LEDs with wdt_ccvr
*LEDR_ptr = *wdt_ccvr >> 16;
}
// Key released - Reset WDT
*wdt_crr = 0x76;
}
}
START
KEY still pressed?
KEY pressed?
Update LEDs with WDT CCVR
Reset WDT
Update LEDs with WDT CCVR
FALSE
FALSE
4
TRUE 3
TRUE 2
Button
1 2 3 4 1
1

## Slide 29: Arm General Purpose Registers

## Slide 30: Branching – function calls – subroutines!

## Slide 31: Branching – function calls – subroutines!

## Slide 32: Branching – function calls – subroutines!

## Slide 33: Branching – function calls – subroutines!

## Slide 34: Stack
Base Addr. End Addr. I/O Peripheral
0xFFFF0000 0xFFFFFFFF Arm A9 64kB On-chip Memory for ARM Stack/Heap
0xFFFEC600 0xFFFEC60F Arm A9 Private Timer
0xFFD02000 0xFFD020FC Arm A9 Watchdog Timer (CPU 0)
0xFF709000 0xFF709060 Arm A9 GPIO 1
0xFF204000 0xFF20401F 8-Channel 12-bit ADC
0xFF203040 0xFF20304F Audio System
0xFF203030 0xFF203037 Character Buffer Control
0xFF203020 0xFF20302F Pixel Buffer Control
0xFF203000 0xFF20301F Audio/video Configuration
0xFF202020 0xFF20202F Second Interval Timer
0xFF202000 0xFF20201F Interval Timer
0xFF201020 0xFF201027 Infrared (IrDA)
0xFF201000 0xFF20100F 2x JTAG UART
0xFF200108 0xFF20010F PS/2 (Secondary Port)
0xFF200100 0xFF200107 PS/2 (Primary Port)
0xFF200090 0xFF20009F Mandelbrot Generator
0xFF200070 0xFF20008F GPIO 1 (JP2) I/O Expansion
0xFF200060 0xFF20006F GPIO 0 (JP1) LT24 LCD & Touchscreen
0xFF200050 0xFF20005F KEY[3-0] Push Buttons
0xFF200040 0xFF20004F SW[9-0] Slide Switches
0xFF200030 0xFF20003F HEX[5-4] 7-segment Displays
0xFF200020 0xFF20002F HEX[3-0] 7-segment Displays
0xFF200000 0xFF20000F LEDR[9-0] Red LEDs
0xC9000000 0xC9001FFF VGA Character Buffer
0xC8000000 0xC8003FFF 16kB FPGA On-chip SRAM
0xC4000000 0xC7FFFFFF 64MB DDR SDRAM - VGA Pixel Buffer
0xC0000000 0xC000FFFF 64kB FPGA On-chip SRAM for ARM Instructions
0x01000040 0x3FFFFFFF 1GB DDR3 Memory
0x00000000 0x0100003F Shadow Boot ROM and Preloader
0xFFFF FB00
0xFFFF 0000
0xFFFF FFFF
0xC000 0000
0xC000 FFFF
0x0000 0000

## Slide 35: Stack Operation
0xFFFF FB00
0xFFFF 0000
0xFFFF EFFF MPU L2 cache controller - Stray here and you’ll crash the processor!

## Slide 36: Function Pointers
int aFunction(int a, int b) {
int c = a + b;
return c;
}
int anotherFunc(int a, int b) {
int c = a * b;
return c;
}
As the function is simply code in memory,
you can in fact create a pointer to the function.
typedef int (*TaskFunction)(int, int);
int main(void) {
// Create a pointer to aFunction.
TaskFunction aPointer = &aFunction;
// Create some inputs
int a = 4;
int b = 6;
// Try calling the function
int c = aPointer(a, b);
// Do nothing, forever.
while (1) {
HPS_ResetWatchdog();
}
}

## Slide 37: Questions