## Slide 1: ELEC5620M Embedded Microprocessor System Design
Unit 2
Dr David Cowell Module Leader d.m.j.cowell@leeds.ac.uk
Prof Steven Freear

## Slide 2: GitHub Classrooms
66 candidates have not signed up to GitHub Classrooms for ELEC5620M! 62 of 66 collected DE1-SoC Hardware. Cannot pass ELEC5620M without using GitHub. Not engaged. 87 candidates have not used Committed AND Pushed any code to GitHub! Commit code and push from GitHub desktop (See GitHub Intro lecture). Check GitHub.com code shows.

## Slide 3: ELEC5620M Assessment Summary
Note overlapping assessments
ELEC5566M

## Slide 4: ELEC5620M Embedded Microprocessor System Design
Assignment 1 Deadline 11th March 2024 at 2pm
Dr David Cowell Module Leader d.m.j.cowell@leeds.ac.uk
Prof Steven Freear

## Slide 5: Minerva > ELEC5620M > Assessment and Feedback Assignment 1 – Unit 1: Design Task
Seven Segment Display Driver – Guided Design Task
Use Template repository provided ELEC5620M-Assessment1 Link on Minerva to create your repository
2 page written report
Incremental GitHub code commits of C code
Github online documentation using the readme
Read and follow guidance in assignment brief carefully
30% of module – Read rubric on Minerva and use to guide your submission.
Deadline Monday 13th March 2023 at 2pm
  5% per day (or part of) penalty subtracted for late submission.
  All request for extensions/mit. circs. from the Student Support Office (electronics@leeds.ac.uk)

## Slide 6: Minerva > ELEC5620M > Assessment and Feedback Assignment 1 – Unit 1: Design Task
  ELEC5620M Assignment 1 - Briefing Document The technical task, rules and information.
  ELEC5620M Assignment 1 - GitHub Classrooms Repository Supplied code – You must incrementally commit your changes from GitHub Desktop – not web interface!
  ELEC5620M Combined GitHub, Coding and Hardware Testing Rubric The marking rubric – read it to understand what qualities we are looking for to award marks.
  ELEC5620M Assignment 1 - Turnitin Report Submission Your report is uploaded here.

## Slide 7: ELEC5620M Combined GitHub, Coding and Hardware Testing Rubric

## Slide 8: Assignment 1: Seven Segment Display Driver

## Slide 9: Assignment 1: Seven Segment Display Driver

## Slide 10: Assignment 1: Seven Segment Display Driver

## Slide 11: Unit 1.2:
Task recap

## Slide 12: Unit 1.2 Task Recap
volatile unsigned int *ledr_ptr = (unsigned int *) 0xFF200000;
volatile unsigned int *switch_ptr = (unsigned int *) 0xFF200040;
int main(void) {
while (1) {
*ledr_ptr = *switch_ptr;
HPS_ResetWatchdog();
}
}
volatile unsigned int *ledr_ptr = (unsigned int *) 0xFF200000;
volatile unsigned int *switch_ptr = (unsigned int *) 0xFF200040;
#define LSC_BASE_KEYS ((unsigned char*)0xFF200050)
volatile unsigned int *key_ptr = (unsigned int *)LSC_BASE_KEYS;
int main(void) {
while (1) {
if(*key_ptr) *ledr_ptr = *switch_ptr;
else *ledr_ptr = ~*switch_ptr;
HPS_ResetWatchdog();
}
}

## Slide 13: Unit 1.2 Task Recap
volatile unsigned int *ledr_ptr = (unsigned int *) 0xFF200000;
volatile unsigned int *switch_ptr = (unsigned int *) 0xFF200040;
volatile unsigned int *key_ptr = (unsigned int *) 0xFF200050;
volatile unsigned char *sevenseg03_ptr = (unsigned char *) 0xFF200020; // 7-segment HEX[3-0]
int main(void) {
while (1) {
if(*key_ptr) *ledr_ptr = *switch_ptr;
else *ledr_ptr = ~*switch_ptr;
*sevenseg03_ptr = *switch_ptr & (0x7F); // Display SW[6-0] on HEX[0]
*(sevenseg03_ptr + 3) = *switch_ptr & (0x7F); // Display SW[6-0] on HEX[3]
HPS_ResetWatchdog();
}
}

## Slide 14: Unit 1.2 Task Recap

## Slide 15: Unit 1.2 Task Recap
Click + and select Stack

## Slide 16: Unit 1.2 Task Recap

## Slide 17: Unit 1.2 Task Recap
0xFFFF …FAE0 | …FAE0 | …FAE0 | …FAE0 | …FAE0
…FAC8 |  |  |  | …FAC8
 | …FAB0 |  |  | …FAB0
 |  | …FA98 |  | …FA98
 |  |  | …FA80 | …FA80
 |  |  |  | …FA68
18 byte difference
6x 32-bit words
18 byte difference
Stack is 0xFB00 bytes.
(0xFAB0 = 64,176)
64,256 / 18 = 2674
Testing: 2675 recursions

## Slide 18: Unit 1.2 Task Recap
Source: https://en.wikipedia.org/wiki/Summation

## Slide 19: Unit 1.2 Task Recap
int main(void) {
// Create a pointer to aFunction.
TaskFunction aPointer = &aFunction;
// Create some inputs
int a = 4;
int b = 6;
// Create a pointer to aFunction.
TaskFunction aPointer = &aFunction;
int c = aPointer(a, b); // returns c = a + b
// Update pointer to anotherFunc.
aPointer = &anotherFunc;
int c = aPointer(a, b); // returns c = a * b
// Do nothing, forever.
while (1) {
HPS_ResetWatchdog();
}
}
// Define a new data type for a function pointers
typedef int (*TaskFunction)(int, int);
int aFunction(int a, int b) {
int c = a + b;
return c;
}
int anotherFunc(int a, int b) {
int c = a * b;
return c;
}

## Slide 20
Unit 2.1
Structuring Software Flow
  Polling
  Non-Blocking vs Blocking
Timers
  A9 Private Timer
Event Schedulers
Use GitHub Classrooms link on Minerva to create your personal Unit 2 repository!

## Slide 21: Background: Software Flow Polling 1-1-HelloWatchdog

## Slide 22: Background: Software Flow Polling 1-1-HelloWatchdog

## Slide 23: Background: Software Flow Polling 1-1-HelloWatchdog
if(false)

## Slide 24: Background: Software Flow Polling 1-1-HelloWatchdog
if(true)

## Slide 25: Background: Software Flow Non-blocking vs Blocking
Non-blocking
Bypasses if event not occurred
Blocking
Waits for event to occur

## Slide 26: Background: Software Flow Non-blocking vs Blocking
Non-blocking
Bypasses if event not occurred
Blocking
Waits for event to occur
WAIT
WAIT

## Slide 27: Event Timers
Watchdog Timer – Resets system when reaches zero!
A9 Private Timers
  Cyclone V SoC Hard Processor System (HPS) has MANY other timers.
Timers allow event control with precise timing, delay, frequency etc

## Slide 28: ARM A9 Private Timer Pointers

## Slide 29: ARM A9 Private Timer Control – Bit manipulation
E 1<<0 0001 | Bitwise OR
A 1<<1 0010 |
I 0<<2 0000 |
Prescaler 0<<8 000000000 |
000000011

## Slide 30: ARM A9 Private Timer Example use

## Slide 31: Controlling Timed Events
unsigned int lastBlinkTimerValue = *private_timer_value;
const unsigned int blinkPeriod = 100000000;
while(1) {
// Read the current time
unsigned int currentTimerValue = *private_timer_value;
// Check if it is time to blink
if ((lastBlinkTimerValue - currentTimerValue) >= blinkPeriod) {
*LEDR_ptr = ~(*LEDR_ptr); // Invert the LEDs
lastBlinkTimerValue = lastBlinkTimerValue - blinkPeriod;
}
}

## Slide 32: Controlling Timed Events
unsigned int lastBlinkTimerValue = *private_timer_value;
const unsigned int blinkPeriod = 100000000;
while(1) {
// Read the current time
unsigned int currentTimerValue = *private_timer_value;
// Check if it is time to blink
if ((lastBlinkTimerValue - currentTimerValue) >= blinkPeriod) {
*LEDR_ptr = ~(*LEDR_ptr); // Invert the LEDs
lastBlinkTimerValue = lastBlinkTimerValue - blinkPeriod;
}
}
Unsigned
Wraparound
Arithmetic
e.g.
0x0001
-0x0002
=0xFFFF

## Slide 33: Task: Controlling Multiple Events
unsigned int lastBlinkTimerValue[2] = {0,0};
const unsigned int blinkPeriod[2] = {100000000,5000};
while(1) {
// Read the current time
unsigned int currentTimerValue = *private_timer_value;
// Timer loop 1
if ((lastBlinkTimerValue[1] - currentTimerValue) >= blinkPeriod[1]) {
*LEDR_ptr = ~(*LEDR_ptr); // Invert the LEDs
lastBlinkTimerValue[1] = lastBlinkTimerValue[1] – blinkPeriod[1];
}
// Timer loop 2
if ((lastBlinkTimerValue[2] - currentTimerValue) >= blinkPeriod[2]) {
...

## Slide 34: Task Schedulers
//Define new data type for function which takes an int parameter and returns nothing.
typedef void (*TaskFunction)(int);
void toggle (int id){
volatile unsigned int *LEDR_ptr = (unsigned int *) 0xFF200000;
unsigned int ledVal = *LEDR_ptr; //Read
ledVal = (ledVal ^ (1 << id)); //Modify. Use XOR to toggle LED "id"
*LEDR_ptr = ledVal; //Write
}
TaskFunction taskFunctions[taskCount] = {&toggle,&toggle,&toggle,&invert};
for (taskID = 0; taskID < taskCount; taskID++) {
if ((taskLastTime[taskID] - currentTimerValue) >= taskInterval[taskID]) {
// When the task is ready to be run, call function, using Function Pointer
taskFunctions[taskID](taskID);
taskLastTime[taskID] = taskLastTime[taskID] - taskInterval[taskID];
}
}

## Slide 35: Read-Modify-Write Bit manipulation
void toggle (int id){
volatile unsigned int *LEDR_ptr = (unsigned int *) 0xFF200000;
unsigned int ledVal = *LEDR_ptr; //Read
ledVal = (ledVal ^ (1 << id)); //Modify. Use XOR to toggle LED "id"
*LEDR_ptr = ledVal; //Write
}
Setting a bit
Use the bitwise OR operator (|)
(combined bitshift left (<<))
to set n-th bit of ledVal to 1.
ledVal = (ledVal | (1 << n));
Clearing a bit
Use the bitwise AND operator (&) (combined bitwise NOT (~) and bitshift left (<<)) to set the n-th bit of ledVal to 0.
ledVal = (ledVal & ~(1 << n));
Changing the n-th bit to x
One method is to clear the specific bit, then set the specific bit as above.
ledVal = (ledVal & ~(x << n)) | (1 << n));
Toggling a bit
Use the bitwise XOR operator (^) (combined bitshift left (<<))
to toggle the n-th bit of ledVal.
ledVal = (ledVal ^ (1 << n));
Checking a bit
Use bitshift right (>>)) to move n-th bit to Least Significant Bit (LSB) then check bit using a bitwise AND operator (&)
ledVal = ((ledVal >> n) & 0x1);

## Slide 36: Questions?