## Slide 1: ELEC5620M Embedded Microprocessor System Design
Unit 2.1 Task Recap
Unit 2.2
Dr David Cowell Module Leader d.m.j.cowell@leeds.ac.uk
Prof Steven Freear

## Slide 2: GitHub Classrooms
Commit code and push from GitHub desktop (See GitHub Intro lecture). Check GitHub.com code shows.

## Slide 3: ELEC5620M Assessment Summary
ELEC5566M

## Slide 4: ELEC5620M Embedded Microprocessor System Design
Assignment 1 Deadline 11th March 2024 at 2pm
Dr David Cowell Module Leader d.m.j.cowell@leeds.ac.uk
Prof Steven Freear

## Slide 5: ELEC5620M Combined GitHub, Coding and Hardware Testing Rubric

## Slide 6: Unit 1.2:
Task recap

## Slide 7: Arm A9 Private Timer Registers

## Slide 8: A9 Private Timer Memory Mapped Interface
#define LSC_BASE_PRIV_TIM ((unsigned char*)0xFFFEC600)

## Slide 9: A9 Private Timer Memory Mapped Interface
#define LSC_BASE_PRIV_TIM ((unsigned char*)0xFFFEC600)
// ARM A9 Private Timer Value
volatile unsigned int *private_timer_value = (unsigned int *)(((unsigned char*)0xFFFEC600) + 0x4);
// ARM A9 Private Timer Value
volatile unsigned int *private_timer_value = (unsigned int *)(0xFFFEC604);

## Slide 10: A9 Private Timer Task 1 – Timer clock frequency?

## Slide 11: A9 Private Timer Task 1 – Timer clock frequency?

## Slide 12: A9 Private Timer Task 1 – Timer equation

## Slide 13: A9 Private Timer Task 1 – Timer clock frequency

## Slide 14: A9 Private Timer Task 1 – Timer clock frequency
16 timer periods = 7.36 seconds … 1 period = 0.46 seconds
32 timer periods = 14.23 seconds … 1 period = 0.44 seconds

## Slide 15: A9 Private Timer Task 1 – Timer clock frequency
16 timer periods = 7.36 seconds … 1 period = 0.46 seconds
32 timer periods = 14.23 seconds … 1 period = 0.44 seconds
Work out the clock frequency that drives the timer

## Slide 16: A9 Private Timer Task 2 – Non-Blocking Timer - Count rate
1 second count rate Load_value = 249999999 !

## Slide 17: A9 Private Timer Task 2 – Non-Blocking Timer
const unsigned int blinkPeriod = 224999999;
unsigned int counter; //Create a local counter variable and initialise
counter = 0;
while(1) {
unsigned int currentTimerValue = *private_timer_value;
if ((lastBlinkTimerValue - currentTimerValue) >= blinkPeriod) {
counter = counter+1; //Increment the counter
lastBlinkTimerValue = lastBlinkTimerValue - blinkPeriod;
}
if (*private_timer_interrupt & 0x1) {
// If the timer interrupt flag is set, clear the flag
*private_timer_interrupt = 0x1;
}
*LEDR_ptr = counter & 0x3FF; // Use bitmasking to ensure only valid bits are set.
HPS_ResetWatchdog();
}

## Slide 18: Task 3

## Slide 19: Task 3 - Possible solution
/*
* This program provides a non-blocking example of code for the ARM A9 Private Timer
*/
#include "HPS_Watchdog/HPS_Watchdog.h"
#include "DE1SoC_Addresses/DE1SoC_Addresses.h"
#define MAX_LEDS 3
//Main Function
int main(void) {
/* Pointers to peripherals */
// Red LEDs base address
volatile unsigned int *LEDR_ptr = (unsigned int *) LSC_BASE_RED_LEDS;
// ARM A9 Private Timer Load
volatile unsigned int *private_timer_load = (unsigned int *)(LSC_BASE_PRIV_TIM + 0x0);
// ARM A9 Private Timer Value
volatile unsigned int *private_timer_value = (unsigned int *)(LSC_BASE_PRIV_TIM + 0x4);
// ARM A9 Private Timer Control
volatile unsigned int *private_timer_control = (unsigned int *)(LSC_BASE_PRIV_TIM + 0x8);
// ARM A9 Private Timer Interrupt
volatile unsigned int *private_timer_interrupt = (unsigned int *)(LSC_BASE_PRIV_TIM + 0xC);
/* Initialisation */
// Configure the ARM Private Timer
// Set the "Load" value of the timer to max value:
*private_timer_load = 0xFFFFFFFF;
// Set the "Prescaler" value to 0, Enable the timer (E = 1), Set Automatic reload
// on overflow (A = 1), and disable ISR (I = 0)
*private_timer_control = (0 << 8) | (0 << 2) | (1 << 1) | (1 << 0);
/* Main Run Loop */
/* Local Variables */
unsigned int lastBlinkTimerValue[MAX_LEDS] = {0};
unsigned int task;
unsigned int currentTimerValue;
//Set Timer Rate
const unsigned int blinkPeriod[MAX_LEDS] = {224999999,22499999,2249999}; // PERIPHCLK=225MHz
while(1) {
// Check if it is time to blink
for(task = 0; task < MAX_LEDS; task++){
// Read the current time
currentTimerValue = *private_timer_value;
if ((lastBlinkTimerValue[task] - currentTimerValue) >= blinkPeriod[task]) {
//Invert the required LED
*LEDR_ptr = (*LEDR_ptr ^ (1 << task));
//Update the last blink timer values
lastBlinkTimerValue[task] = lastBlinkTimerValue[task] - blinkPeriod[task];
}
}
if (*private_timer_interrupt & 0x1) {
// If the timer interrupt flag is set, clear the flag
*private_timer_interrupt = 0x1;
}
// Finally, reset the watchdog timer.
HPS_ResetWatchdog();
}
}

## Slide 20: Task 3 - Possible solution
/* Initialisation */
// Configure the ARM Private Timer
// Set the "Load" value of the timer to max value:
*private_timer_load = 0xFFFFFFFF;
// Set the "Prescaler" value to 0, Enable the timer (E = 1), Set Automatic reload
// on overflow (A = 1), and disable ISR (I = 0)
*private_timer_control = (0 << 8) | (0 << 2) | (1 << 1) | (1 << 0);
/* Main Run Loop */
/* Local Variables */
unsigned int lastBlinkTimerValue[MAX_LEDS] = {0};
unsigned int task;
unsigned int currentTimerValue;
//Set Timer Rate
const unsigned int blinkPeriod[MAX_LEDS] = {224999999,22499999,2249999}; // PERIPHCLK=225MHz
while(1) {
// Check if it is time to blink
for(task = 0; task < MAX_LEDS; task++){
// Read the current time
currentTimerValue = *private_timer_value;
if ((lastBlinkTimerValue[task] - currentTimerValue) >= blinkPeriod[task]) {
//Invert the required LED
*LEDR_ptr = (*LEDR_ptr ^ (1 << task));
//Update the last blink timer values
lastBlinkTimerValue[task] = lastBlinkTimerValue[task] - blinkPeriod[task];
}
}
if (*private_timer_interrupt & 0x1) {
// If the timer interrupt flag is set, clear the flag
*private_timer_interrupt = 0x1;
}
// Finally, reset the watchdog timer.
HPS_ResetWatchdog();
}
}

## Slide 21: Task 3 - Possible solution
while(1) {
// Check if it is time to blink
for(task = 0; task < MAX_LEDS; task++){
// Read the current time
currentTimerValue = *private_timer_value;
if ((lastBlinkTimerValue[task] - currentTimerValue) >= blinkPeriod[task]) {
//Invert the required LED
*LEDR_ptr = (*LEDR_ptr ^ (1 << task));
//Update the last blink timer values
lastBlinkTimerValue[task] = lastBlinkTimerValue[task] - blinkPeriod[task];
}
}
if (*private_timer_interrupt & 0x1) {
// If the timer interrupt flag is set, clear the flag
*private_timer_interrupt = 0x1;
}
// Finally, reset the watchdog timer.
HPS_ResetWatchdog();
}
}

## Slide 22
Unit 2.2
Bare Metal Drivers
  Servo Motor Driver
  A9 Private Timer Driver Task

## Slide 23: Task: Servo Driver
Servo_initialise(0xFF2000C0), //Initialise Servo Controller
Servo_enable(0, true), //Enable Servo 0.
Servo_pulseWidthRange(0, true), //Double pulse width.

## Slide 24: Bare Metal Drivers Structure

## Slide 25: Servo and LCD Connection

## Slide 26: Example Servo Driver use
Useful debugging tool – allows break point upon a driver error

## Slide 27: Example Servo Driver use
Custom datatype to contain all information about our Servo Driver!
Simple initialisation functions
Simple operational functions
No pointers manually coded in the main function!

## Slide 28: Driver Contexts
Utils/driver_ctx.h
DE1SoC_Servo.h

## Slide 29: Servo Driver Initialisation functions DE1SoC_Servo.c

## Slide 30: Servo Driver Initialisation functions DE1SoC_Servo.c

## Slide 31: Servo Driver User Facing Enable Function

## Slide 32: Servo Driver User Facing Enable Function

## Slide 33: Pointer, addresses and arrays
volatile unsigned char* servo_ptr = (unsigned char*)&ctx->base[channel]; //Array notation
volatile unsigned char* servo_ptr = (unsigned char*)&(ctx->base[channel]); //Brackets clarify address
volatile unsigned char* servo_ptr = (unsigned char*)&*(ctx->base); //Without array of base addresses
array_value: (ctx->base[channel]);
array_address: &(ctx->base[channel]);
pointer_value: *(ctx->base);
pointer_address: &*(ctx->base);

## Slide 34: Servo Driver User Facing Enable Function
Manipulation of servo_ptr value will directly update the
memory mapped peripheral!!!

## Slide 35: Main Task
//Read Back Current Value from A9 Timer
HpsErr_t Timer_currentValue( PTimerCtx_t ctx, unsigned int* value);
How can we read a value when our return value is an error flag?

## Slide 36: Returning multiple values - Pass by Reference
unsigned int swap(int* a, int* b)
{
// Access input arguments values using pointers
int temp = *a;
*a = *b; //Manipulate pointer values
*b = temp;
return 0; //Return success
}
...
int main(void)
{
int x = 123;
int y = 456;
swap(&x, &y); // Pass address of variables as inputs to function
// Now, x=456 & y=123
return 0;
}

## Slide 37: Return currentValue using - Pass by value
PTimerCtx_t timerCtx;
unsigned int timerCurrentValue;
...
exitOnFail(
Timer_currentValue(timerCtx, &timerCurrentValue), //Enable Timer Controller
ERR_SUCCESS); //Exit if not successful
//Read Back Current Value from A9 Timer
HpsErr_t Timer_currentValue( PTimerCtx_t ctx, unsigned int* value) {
HpsErr_t status = DriverContextValidate(ctx);
if (IS_ERROR(status)) return status;
// Read the Current Timer Value.
volatile unsigned int* timer_ptr = (unsigned int*)&ctx->base[0];
unsigned int temp;
temp = timer_ptr[TIMER_VALUE];
*value = temp;
return ERR_SUCCESS;
}

## Slide 38: Questions?