## Slide 1: Physiological signal introduction and processing
Dr Zhiqiang Zhang
School of Electronic and Electrical Engineering
School of Mechanical Engineering
Faculty of Engineering and Physical Sciences
Email: z.zhang3@leeds.ac.uk
Room: EEE 1.69

## Slide 2: Functional Characteristics
Contractility
Extensibility
Excitability
Notes: Ability to receive and respond to a stimuli

## Slide 3: Sequence in skeletal muscle contraction

## Slide 4: EMG basic
Motor unit
  The smallest functional unit to describe the neural control of the muscular contraction process
  The motor neuron, situated in the spinal cord, has a long axon which goes to the muscle.
  Each axon splits up into a number of branches each of which ends on a motor endplate on a muscle fibre.
  Ensemble of a motor neuron and the muscle fibres it innervates is called the motor unit.

## Slide 5: EMG basic
Motor Unit Action Potential
  Typically, each motor-neuron innervates several hundred muscle fibers (innervation ratio)
  Motor Unit Action Potential (MUAP) = summed electrical activity of all muscle fibers activated within the motor unit
  Muscle force increased through higher recruitment and increased rate coding

## Slide 7: Types of EMG electrodes
Inserted
  Fine-wire (Intra Musular)
  Needle
  Implanted
Surface
  Extramuscular

## Slide 8: Fine-wire/Needle Electrodes
Advantages
  Extremely sensitive
  Record the activity of a single motor unit
  Access to deep musculature
  Little cross-talk concern
Disadvantages
  Requires medical personnel, certification
  Repositioning nearly impossible
  Detection area may not be representative of entire muscle

## Slide 9: Surface Electrodes
Advantages
  Quick, easy to apply
  No medical supervision, nor required certification
  Minimal discomfort
  Easy to reposition
  Disposable
Disadvantages
  Generally used only for superficial muscles
  Cross-talk concerns
  No standard electrode placement
  May affect movement patterns of subject
The most common and widely used in practice

## Slide 10: Surface electrode placement
The surface EMG electrodes should be placed
  between the motor unit and the tendinous insertion of the muscle,
  along the longitudinal midline of the muscle
  Electrode alignment with the direction of muscle fibres to increase probability of detecting same signal

## Slide 11
When the electrodes are arranged in this way, the detecting surfaces intersect most of the same muscle fibres, and as a result, an improved superimposed signal is observed.

## Slide 12: Factors influencing the EMG signal
The quality of the detected sEMG signal determines the usefulness of the information extracted from the sEMG signal.
It is of high importance to maximise the quality of the acquired signal.
The quality of the acquired signal depends on:
  Sensor location (upon the middle of muscle belly)
Notes: The human body is a good electrical conductor, but unfortunately the electrical conductivity varies with tissue type, thickness (Fig. 14), physiological changes and temperature

## Slide 13: Factors influencing the EMG signal
The quality of the detected sEMG signal determines the usefulness of the information extracted from the sEMG signal.
It is of high importance to maximise the quality of the acquired signal.
The quality of the acquired signal depends on:
  Sensor location (upon the middle of muscle belly)
  Tissue characteristics
Notes: The human body is a good electrical conductor, but unfortunately the electrical conductivity varies with tissue type, thickness (Fig. 14), physiological changes and temperature

## Slide 14
Notes: The human body is a good electrical conductor, but unfortunately the electrical conductivity varies with tissue type, thickness (Fig. 14), physiological changes and temperature

## Slide 15: Factors influencing the EMG signal
The quality of the detected sEMG signal determines the usefulness of the information extracted from the sEMG signal.
It is of high importance to maximise the quality of the acquired signal.
The quality of the acquired signal depends on:
  Sensor location (upon the middle of muscle belly)
  Tissue characteristics
  Cross-talk from other muscles
Notes: The human body is a good electrical conductor, but unfortunately the electrical conductivity varies with tissue type, thickness (Fig. 14), physiological changes and temperature

## Slide 17: Factors influencing the EMG signal
The quality of the detected sEMG signal determines the usefulness of the information extracted from the sEMG signal.
It is of high importance to maximise the quality of the acquired signal.
The quality of the acquired signal depends on:
  Sensor location (upon the middle of muscle belly)
  Tissue characteristics
  Cross-talk from other muscles
  Noise contamination
Notes: The human body is a good electrical conductor, but unfortunately the electrical conductivity varies with tissue type, thickness (Fig. 14), physiological changes and temperature

## Slide 18: EMG signal processing
Time-Frequency Analysis:
Short-time Fourier Transform
Wavelet Transform
Frequency Domain
FFT Analysis
Frequency spectrum
Mean frequency
Median frequency
Time Domain
Rectification
Smoothing
Filtering
Amplitude Normalization
…

## Slide 19: Time Domain Vs Frequency
Fourier Transformations
  a signal can be considered as a summation of sine waves with different frequency
  The FFT algorithm can be described as a decomposition of the EMG signal to its underlying sinus contents

## Slide 21: Time Domain: Rectification
Only positive values are analysed
Half-wave rectification
  all negative data is discarded
  positive data is kept.
Full-wave rectification
  the absolute value of each data point is used
Full-wave is preferred

## Slide 22: Example

## Slide 23: Example

## Slide 24: Smoothing
Outline the mean trend of signal development
  cutting away steep amplitude spikes
  Receiving a amplitude envelop
Moving average
Root mean square
Notes: Moving Window

## Slide 25: Moving Window

## Slide 26: Example
For any signal the M point mean average is y

## Slide 29: Why rectification and moving average???
A healthy well organized muscle in regular conditions turns off if it is not needed anymore.
If it still stays on, it is an indicator for
  active muscle spasm,
  reflex induced (e.g. pain) hypertonus
  joint instability
  behavioural disuse (stress, bad muscle coordination).
Notes: The flexion-relaxation phenomenon. When
slowly bending forward from an upright position, the
back muscles (ch.1 multifidii) and hip extensors (ch. 2
gluteus maximus) turn off at the most flexed position
(dashed vertical line and video picture). The limb
momentum is held by passive structures like ligaments.
When slowly extending back, both muscles
start firing again. Other synergists (ch. 3 hamstrings)
are active all the time. Low back pain patients can lack
this innervation silence due to dysfunction or pain.

## Slide 31: Power Spectrum

## Slide 32: Example
Hz
Power

## Slide 33: Solution

## Slide 34: Solution

## Slide 35: Fatigue analysis
It can be used to identify weak muscles. The most famous application of frequency shifts is in the analysis of low back pain patient
it can be used to prove the efficiency of strength training exercises
  Training induced short term fatigue is the preliminary condition for muscle growth
Notes: Schematic illustration of the frequency shift towards lower
frequencies in sustained contractions and calculation of the muscle
fatigue index.
Typical test arrangement and findings for static back
endurance tests: Median (A), Mean Frequency (B),

## Slide 37: Example (previous example paper)
John is doing some push up and the table below is the median frequency and corresponding mean frequency of his Biceps Brachii muscle during the exercises. Please identify at which five columns are most likely the fatigue happens and why?

## Slide 39: How to use EMG to control prosthetic arm

## Slide 40: More complex EMG signal processing
AI or data driven based
Neuromuscular-skeletal model based

## Slide 41
EMG Signal
Time Domain features
Frequency Domain features
Training
AI
Controller
Prosthetic device
AI based

## Slide 42
EMG Signal
Time Domain features
Frequency Domain features
Training
AI
Controller
Prosthetic device
AI based
Deep learning

## Slide 43: Model-based